TD –DHCP

Exercice n°1: Analyse d'un échange DHCP

Soit 6 entêtes de trames  issues d'un échange entre  un serveur et un client DHCP

No. Time      Source         Destination      Protocol Info

1 0.000000  0.0.0.0        255.255.255.255  DHCP     DHCP Discover - Transaction ID 0x6719436e

2 0.001182  192.168.0.253  192.168.0.9      ICMP     Echo (ping) request

3 0.342454  192.168.0.253  192.168.0.9      DHCP     DHCP Offer    - Transaction ID 0x6719436e

4 0.344405  0.0.0.0        255.255.255.255  DHCP     DHCP Request  - Transaction ID 0x6719436e

5 0.348264  192.168.0.253  192.168.0.9      DHCP     DHCP ACK      - Transaction ID 0x6719436e

6 0.353014  CIS_b9:49:37   Broadcast        ARP      Who has 192.168.0.9?  Tell 192.168.0.9

Expliquez le rôle de chaque trame :

Vous donnerez sa provenance, sa destination, son type et son rôle.

Exercice n°2: Analyse détaillée de la trame DHCP DISCOVER

Commentez pour chaque trame, les lignes surlignées en jaune.

Frame 1 (342 bytes on wire, 342 bytes captured)

Arrival Time: Dec 10, 2002 10:10:04.658425000

Time delta from previous packet: 0.000000000 seconds

Time relative to first packet: 0.000000000 seconds

Frame Number: 1

Packet Length: 342 bytes

Capture Length: 342 bytes

Ethernet II, Src: 00:20:18:b9:49:37, Dst: ff:ff:ff:ff:ff:ff

Destination: ff:ff:ff:ff:ff:ff (Broadcast)

Source: 00:20:18:b9:49:37 (CIS_b9:49:37)

Type: IP (0x0800)

Internet Protocol, Src Addr: 0.0.0.0 (0.0.0.0), Dst Addr: 255.255.255.255 (255.255.255.255)

Version: 4

Header length: 20 bytes

Differentiated Services Field: 0x00 (DSCP 0x00: Default; ECN: 0x00)

0000 00.. = Differentiated Services Codepoint: Default (0x00)

.... ..0. = ECN-Capable Transport (ECT): 0

.... ...0 = ECN-CE: 0

Total Length: 328

Identification: 0x4b10

Flags: 0x00

.0.. = Don't fragment: Not set

..0. = More fragments: Not set

Fragment offset: 0

Time to live: 128

Protocol: UDP (0x11)

Header checksum: 0xee95 (correct)

Source: 0.0.0.0 (0.0.0.0)

Destination: 255.255.255.255 (255.255.255.255)

User Datagram Protocol, Src Port: bootpc (68), Dst Port: bootps (67)

Source port: bootpc (68)

Destination port: bootps (67)

Length: 308

Checksum: 0xf904 (correct)

Bootstrap Protocol

Message type: Boot Request (1)

Hardware type: Ethernet

Hardware address length: 6

Hops: 0

Transaction ID: 0x6719436e

Seconds elapsed: 0

Bootp flags: 0x0000 (Unicast)

0... .... .... .... = Broadcast flag: Unicast

.000 0000 0000 0000 = Reserved flags: 0x0000

Client IP address: 0.0.0.0 (0.0.0.0)

Your (client) IP address: 0.0.0.0 (0.0.0.0)

Next server IP address: 0.0.0.0 (0.0.0.0)

Relay agent IP address: 0.0.0.0 (0.0.0.0)

Client hardware address: 00:20:18:b9:49:37

Server host name not given

Boot file name not given

Magic cookie: (OK)

Option 53: DHCP Message Type = DHCP Discover

Unknown Option Code: 251 (1 bytes)

Option 61: Client identifier

Hardware type: Ethernet

Client hardware address: 00:20:18:b9:49:37

Option 50: Requested IP Address = 192.168.0.9

Option 12: Host Name = "pchris"

Option 60: Vendor class identifier = "MSFT 5.0"

Option 55: Parameter Request List

1 = Subnet Mask

15 = Domain Name

3 = Router

6 = Domain Name Server

44 = NetBIOS over TCP/IP Name Server

46 = NetBIOS over TCP/IP Node Type

47 = NetBIOS over TCP/IP Scope

31 = Perform Router Discover

33 = Static Route

43 = Vendor-Specific Information

End Option

Padding

Commentez dans les cadres prévus à cet effet le rôle des champs surlignés.

Exercice n°3: Analyse détaillée de la trame DHCP OFFER

Frame 3 (342 bytes on wire, 342 bytes captured)

Arrival Time: Dec 10, 2002 10:10:05.000879000

Time delta from previous packet: 0.341272000 seconds

Time relative to first packet: 0.342454000 seconds

Frame Number: 3

Packet Length: 342 bytes

Capture Length: 342 bytes

Ethernet II, Src: 00:00:b4:bb:5d:ee, Dst: 00:20:18:b9:49:37

Destination: 00:20:18:b9:49:37 (CIS_b9:49:37)

Source: 00:00:b4:bb:5d:ee (Edimax_bb:5d:ee)

Type: IP (0x0800)

Internet Protocol, Src Addr: 192.168.0.253 (192.168.0.253), Dst Addr: 192.168.0.9 (192.168.0.9)

Version: 4

Header length: 20 bytes

Differentiated Services Field: 0x10 (DSCP 0x04: Unknown DSCP; ECN: 0x00)

0001 00.. = Differentiated Services Codepoint: Unknown (0x04)

.... ..0. = ECN-Capable Transport (ECT): 0

.... ...0 = ECN-CE: 0

Total Length: 328

Identification: 0x0000

Flags: 0x00

.0.. = Don't fragment: Not set

..0. = More fragments: Not set

Fragment offset: 0

Time to live: 16

Protocol: UDP (0x11)

Header checksum: 0x273f (correct)

Source: 192.168.0.253 (192.168.0.253)

Destination: 192.168.0.9 (192.168.0.9)

*** Notez que le serveur fait comme si le client disposait déjà de son adresse IP

User Datagram Protocol, Src Port: bootps (67), Dst Port: bootpc (68)

Source port: bootps (67)

Destination port: bootpc (68)

Length: 308

Checksum: 0xb216 (correct)

Bootstrap Protocol

Message type: Boot Reply (2)

Hardware type: Ethernet

Hardware address length: 6

Hops: 0

Transaction ID: 0x6719436e

Seconds elapsed: 0

Bootp flags: 0x0000 (Unicast)

0... .... .... .... = Broadcast flag: Unicast

.000 0000 0000 0000 = Reserved flags: 0x0000

Client IP address: 0.0.0.0 (0.0.0.0)

Your (client) IP address: 192.168.0.9 (192.168.0.9)

Next server IP address: 192.168.0.253 (192.168.0.253)

Relay agent IP address: 0.0.0.0 (0.0.0.0)

*** Il n'y a pas d'agent de relais DHCP

Client hardware address: 00:20:18:b9:49:37

Server host name not given

Boot file name not given

Magic cookie: (OK)

Option 53: DHCP Message Type = DHCP Offer

Option 54: Server Identifier = 192.168.0.253

Option 51: IP Address Lease Time = 1 hour

Option 1: Subnet Mask = 255.255.255.0

Option 15: Domain Name = "maison.mrs"

Option 3: Router = 192.168.0.253

Option 6: Domain Name Server = 192.168.0.253

End Option

Padding

Commentez dans les cadres prévus à cet effet le rôle des champs surlignés.

Exercice n°4: Analyse détaillée de la trame DHCP REQUEST

Frame 4 (349 bytes on wire, 349 bytes captured)

…….

Ethernet II, Src: 00:20:18:b9:49:37, Dst: ff:ff:ff:ff:ff:ff

Destination: ff:ff:ff:ff:ff:ff (Broadcast)

Source: 00:20:18:b9:49:37 (CIS_b9:49:37)

Type: IP (0x0800)

Internet Protocol, Src Addr: 0.0.0.0 (0.0.0.0), Dst Addr: 255.255.255.255 (255.255.255.255)

…….

User Datagram Protocol, Src Port: bootpc (68), Dst Port: bootps (67)

Source port: bootpc (68)

Destination port: bootps (67)

Length: 315

Checksum: 0xe94b (correct)

Bootstrap Protocol

Message type: Boot Request (1)

Hardware type: Ethernet

Hardware address length: 6

Hops: 0

Transaction ID: 0x6719436e

Seconds elapsed: 0

Bootp flags: 0x0000 (Unicast)

0... .... .... .... = Broadcast flag: Unicast

.000 0000 0000 0000 = Reserved flags: 0x0000

Client IP address: 0.0.0.0 (0.0.0.0)

Your (client) IP address: 0.0.0.0 (0.0.0.0)

Next server IP address: 0.0.0.0 (0.0.0.0)

Relay agent IP address: 0.0.0.0 (0.0.0.0)

Client hardware address: 00:20:18:b9:49:37

Server host name not given

Boot file name not given

Magic cookie: (OK)

Option 53: DHCP Message Type = DHCP Request

Option 61: Client identifier

Hardware type: Ethernet

Client hardware address: 00:20:18:b9:49:37

Option 50: Requested IP Address = 192.168.0.9

Option 54: Server Identifier = 192.168.0.253

Option 12: Host Name = "pchris"

Option 81: Client Fully Qualified Domain Name (10 bytes)

Option 60: Vendor class identifier = "MSFT 5.0"

Option 55: Parameter Request List

1 = Subnet Mask

15 = Domain Name

3 = Router

6 = Domain Name Server

44 = NetBIOS over TCP/IP Name Server

46 = NetBIOS over TCP/IP Node Type

47 = NetBIOS over TCP/IP Scope

31 = Perform Router Discover

33 = Static Route

43 = Vendor-Specific Information

End Option

Exercice n°5: Analyse détaillée de la trame DHCP ACK

Frame 5 (342 bytes on wire, 342 bytes captured)

…….

Ethernet II, Src: 00:00:b4:bb:5d:ee, Dst: 00:20:18:b9:49:37

Destination: 00:20:18:b9:49:37 (CIS_b9:49:37)

Source: 00:00:b4:bb:5d:ee (Edimax_bb:5d:ee)

Type: IP (0x0800)

Internet Protocol, Src Addr: 192.168.0.253 (192.168.0.253), Dst Addr: 192.168.0.9 (192.168.0.9)

…….

User Datagram Protocol, Src Port: bootps (67), Dst Port: bootpc (68)

Source port: bootps (67)

Destination port: bootpc (68)

Length: 308

Checksum: 0xaf16 (correct)

Bootstrap Protocol

Message type: Boot Reply (2)

Hardware type: Ethernet

Hardware address length: 6

Hops: 0

Transaction ID: 0x6719436e

Seconds elapsed: 0

Bootp flags: 0x0000 (Unicast)

0... .... .... .... = Broadcast flag: Unicast

.000 0000 0000 0000 = Reserved flags: 0x0000

Client IP address: 0.0.0.0 (0.0.0.0)

Your (client) IP address: 192.168.0.9 (192.168.0.9)

Next server IP address: 192.168.0.253 (192.168.0.253)

Relay agent IP address: 0.0.0.0 (0.0.0.0)

Client hardware address: 00:20:18:b9:49:37

Server host name not given

Boot file name not given

Magic cookie: (OK)

Option 53: DHCP Message Type = DHCP ACK

Option 54: Server Identifier = 192.168.0.253

Option 51: IP Address Lease Time = 1 hour

Option 1: Subnet Mask = 255.255.255.0

Option 15: Domain Name = "maison.mrs"

Option 3: Router = 192.168.0.251

Option 6: Domain Name Server = 192.168.0.253

End Option

Padding